## Slide 1: Application Assisted Popcorn Preparation
Students: Igor Berendorf
Or Zamir
Supervisor: Roee Mazor
Semester: Spring 2017
NSSL Laboratory 25/10/17

## Slide 2: Project Goals
Exploring Sound Analysis Methods
Real-time Signal Processing
Android Application Development
Making Top-Notch Popcorn
Notes: הצגת מטרת הפרויקט

## Slide 3: Problem Characteristics
510 Popcorn Kernels Per Bag
Pops’ Width ~20ms
Distribution of Pops Over Time:
Chart: Pops Over Time
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 240
 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 8 | 6 | 3 | 7 | 10 | 18 | 25 | 22 | 36 | 50 | 60 | 64 | 67 | 48 | 30 | 22 | 10
Notes: הצגה של נתוני שקית פופקורן
המלצה

## Slide 4: Work Environment

## Slide 5: Challenges
Reliable Pop Detection
Application Development and User Experience
When is the popcorn ready?
Notes: הצגת מטרת הפרויקט

## Slide 6: Recordings Data Set
10 Full Recordings ~4min Each, both high power and low power
Manually identifying pops
Empiric pop distribution by 4 second bins

## Slide 7: Pop Detection
Five pop detection methods tested
Two selected for porting to Java/Android
Precision | Recall | Method
98.0% | 85.3% | Zamir-Berendorf (Derivative)
97.2% | 79.9% | Moving Average
93.6% | 76.8% | Convolution
94.3% | 71.8% | Z-Score
92.1% | 67.2% | Energy Peak Detection

## Slide 8: Zamir Berendorf
Expected noise calculated at the beginning of the recording
Apply second derivative to emphasize pops
Empiric threshold
Anything above threshold is considered a pop

## Slide 9: Original Signal
Zamir Berendorf
Amplitude
Samples x10^4
Absolute
Double Derivative
Apply Threshold
Mark
Noise Removal
Wanted signal remained about the same
Unwanted signal cut by 30%-50%

## Slide 10: Zamir Berendorf – Noisy Signal
Amplitude
Samples x10^4

## Slide 11: Moving Average
Ongoing average calculation
Empiric factor
Anything above threshold is a pop
Notes: לא דורש זכרון נוסף
עיבוד מידע מאוד קל – ולכן מהיר ולא זולל משאבים
החסרונות רלוונטיים בעיקר לתחילה של חלון – גם הרעש וגם פספוס הפצפוצים (Small interval…)

## Slide 12: Original Signal
Amplitude
Samples x10^4
Absolute
Current Average
Mark
Moving Average
Notes: לא דורש זכרון נוסף
עיבוד מידע מאוד קל – ולכן מהיר ולא זולל משאבים
החסרונות רלוונטיים בעיקר לתחילה של חלון – גם הרעש וגם פספוס הפצפוצים (Small interval…)

## Slide 13: Moving Average – Noisy Signal
Amplitude
Samples x10^4

## Slide 14: Detection Flow Diagram
Idle
Gaussian Peak
Interval

## Slide 15: Detection Stages - Idle
Avoid unnecessary calculations and false identifications
Duration based on power setting
Idle
Gaussian Peak
Interval

## Slide 16: Detection Stages - Peak
Idle
Gaussian Peak
Interval
Find the pop-distribution peak
Popcorn is ready only after peak is reached
Pop detection algorithm depends on power setting

## Slide 17: Detection Stages - Interval
Look for interval longer than 2 seconds
When the desired interval is found – announce “DONE”
Pop detection algorithm depends on power setting
Idle
Gaussian Peak
Interval

## Slide 18: The Application
Multi-threaded
Modular
User friendly
User proof
Requires Android 5.0 LOLLIPOP
Notes: עכשיו ניתן להם להתעסק עם האפליקציה

## Slide 19: Detection Stages Graphics

## Slide 20: Video Here
Removed from presentation because it weights 130MB…

## Slide 21: Application Results
Weighted Abs Distance | Precision | Recall | Method
56.2 | 98.7% | 94.9% | Zamir-Berendorf (Derivative)
81.2 | 90.5% | 89.5% | Moving Average
Weighted Abs Distance | Precision | Recall | Method
23.7 | 98.9% | 94.2% | Moving Average
38.4 | 93.2% | 93.6% | Zamir-Berendorf (Derivative)
Low Power Microwave
High Power Microwave
*Results ignore double detections of the same pop
*Weighted abs distance of the detected pops distribution from the measured distribution

## Slide 22: In Conclusion
Application works in semi-quiet environments
  Tested in white noise environments
Requires human presence
What’s next?
  Improved noise filtering using Machine Learning
  IoT integration

## Slide 23: Thank You!